## Slide 1
REFERENCE IMPLEMENTATION • G1–G7 CLOSED
RoboGuardian
Governed execution is more resilient than
open-loop execution when the world changes.
Self-healing robotic control loop
MuJoCo • bimanual dual SO-101 • CPU inference
github.com/rootz-synapsa/roboguardian
G1–G7 PASS
RG
OBSERVE / GOVERN / RECOVER
Notes: Welcome. Today I’m presenting RoboGuardian, a reference implementation of a self-healing robotic control loop built in a bimanual dual SO-101 MuJoCo simulation. The current evidence chain exercises the left-arm pick-and-place task.

## Slide 2
PROBLEM
The world changes. The plan doesn’t.
02
PLAN ONCE
EXECUTE BLIND
100%
failure under disturbance
10 / 10 deterministic trials
results/g3_failure.json
ARM B / OPEN LOOP
B
TARGET
+0.10 m X drift
END STATE
0.30 m OFF TARGET
When observation stops, the plan becomes fiction.
Notes: Open-loop robots plan once and execute blind. If the environment changes mid-execution, the plan becomes fiction. In our baseline, this blindness caused 10 failures in 10 deterministic trials, with the plate ending 0.30 meters from the target.
Evidence: results/g3_failure.json

## Slide 3
APPROACH
Wrap execution in a governance loop
03
01
OBSERVE
Read the world
as it is now
02
EVALUATE
Classify drift
and risk
03
RE-PLAN
Solve from
fresh state
04
EXECUTE
Issue only the
fresh action
FRESH STATE FEEDS THE NEXT CYCLE
RULE: world drift invalidates stale intent
Notes: RoboGuardian wraps execution in a governance loop. We observe the world, evaluate the drift, re-plan from a fresh observation, and execute the fresh action. The key question is how to keep the stale plan from slipping through during recovery.

## Slide 4
SECTION 18 GUARANTEE
Stale plans never reach the actuators
04
trace = RecoveryTrace(
stale_target=dict(stale_target)
)
fresh_state = provider.observe(...)
ik = solve_arm_ik(
goal_pos=fresh_state.observed_pose,
seed_qpos={...stale_target...}
)
trace.fresh_target = ik["joint_solution_rad"]
_execute_arm(trace.fresh_target, ...)
STALE TARGET
Retained for traceability +
solver initialization only
×
never written
to data.ctrl
FRESH TARGET
ACTUATORS
STRUCTURAL INVARIANT stale_action_executed = False • G5 + G6
IK seed biases the configuration branch (elbow-up/down) only.
The solve goal always comes from fresh observe(). solve_arm_ik() uses an internal MjData copy, so the live simulation remains untouched until _execute_arm(fresh_target).
Notes: This is the core structural guarantee. RoboGuardian retains the stale target for traceability and solver initialization. It may seed the IK optimizer and bias the configuration branch, but goal_pos always comes from fresh_state.observed_pose. solve_arm_ik() creates a fresh MjData internally, so the solve cannot mutate the live simulation. Only fresh_target is passed to _execute_arm and written to data.ctrl.
Evidence: control/recovery.py; control/ik_solver.py; results/g5_recovery.json; results/g6_reliability.json

## Slide 5
EXPERIMENT DESIGN
Apples-to-apples comparison
05
ARM A
HAPPY PATH
No disturbance
Open-loop reference
10 trials
ARM B
OPEN LOOP
Object moved mid-run
No recovery
10 trials
ARM C
ROBOGUARDIAN
Object moved mid-run
Governed recovery
10 trials
COMMON PROTOCOL
SEED 42
NOISE = 0
+0.10 m X
@ BEFORE_GRASP
10 TRIALS / ARM
Notes: We tested three conditions under the same task protocol: Arm A is the undisturbed reference, Arm B is the disturbed open-loop baseline, and Arm C is the disturbed governed loop. Each arm ran 10 trials with seed 42. The disturbance was object_move, plus 0.10 meters in X, triggered before grasp, with noise set to zero. Determinism supports reproducibility; it is not statistical inference.
Evidence: results/g6_reliability.json

## Slide 6
HEAD-TO-HEAD RELIABILITY
Governance restored 10 / 10 success
06
CONTROL / NO DISTURBANCE ARM A 10 / 10
ARM B • OPEN LOOP
0 / 10
STALE EXECUTED 10 / 10
FINAL MISS 0.30 m
ARM C • ROBOGUARDIAN
10 / 10
STALE EXECUTED 0 / 10
RECOVERY 10 / 10
VS
ZERO STALE ACTIONS EXECUTED BY ROBOGUARDIAN
Evidence: results/g6_reliability.json
Notes: The head-to-head result is clear. Arm A succeeded 10 out of 10. Arm B failed 10 out of 10 after the world changed. Arm C recovered 10 out of 10, with zero stale actions executed. This supports the resilience claim under the tested scenario.
Evidence: results/g6_reliability.json; results/g3_failure.json

## Slide 7
VISION PIPELINE • G7
Vision perception without ground truth
07
MEAN POSITION ERROR
≈ 0.7 cm
WORST-CASE ERROR
2.4 cm
MODEL SIZE
≈ 146K params
P50 LATENCY, CPU
ONNX Runtime 0.5 ms
OpenVINO 1.2 ms
OPENVINO VS ONNX RUNTIME
0.44×
speedup ratio
≈2.3× slower on this tiny CPU model
NO SPEEDUP CLAIMED
Both median latencies are below 2 ms. Tail latency remains visible in the G7 artifact.
Notes: The vision pipeline replaces privileged ground-truth detection with CPU inference. The model has about 146 thousand parameters, with roughly 0.7 centimeter mean position error and a worst case of 2.4 centimeters. In g7_openvino.json, ONNX Runtime p50 is 0.542 milliseconds and OpenVINO p50 is 1.230 milliseconds. The reported speedup ratio is baseline divided by OpenVINO, or 0.441. That means OpenVINO is about 2.3 times slower on this tiny model. We claim no speedup. Both median values are below 2 milliseconds, while p95 and maximum latency are higher and remain visible in the artifact.
Evidence: results/g7_openvino.json; results/FINAL_REPORT.md

## Slide 8
EVIDENCE CHAIN
Evidence chain and reproducibility
08
CLAIM
Governed recovery is resilient
GATE
G6 apples-to-apples test
ARTIFACT
results/g6_reliability.json
REPLAY
same seed + same disturbance
results/
├─ g1_environment.json
├─ g2_baseline.json
├─ g3_failure.json
├─ g4_detection_vision_t03.json
├─ g5_recovery_vision.json
├─ g6_reliability.json
└─ g7_openvino.json
G1 PASS
G2 PASS
G3 PASS
G4 PASS
G5 PASS
G6 PASS
G7 PASS
python experiments/run_g6_reliability.py \
--model models/dual_so101_g3.xml \
--trigger before_grasp --delta 0.10 0.0 0.0 --seed 42 --trials 10
Notes: Every quantitative claim resolves to a JSON artifact or append-only event trace. The reproduction command explicitly pins the G6 model, disturbance trigger, delta, seed, and trial count. Repository main commit 71d22dfaff129e1629307a8a788c5ddc7b5bb2b9 contains the updated recovery runner with provider selection, a 0.05 meter task threshold, XY error scoring, clean PLACE IK, and frozen force limits. The G6 runner defaults to dual_so101_g3.xml and applies the same force limits. Both vision evidence files shown on the slide are present in the repository.
Evidence: experiments/run_recovery.py; experiments/run_g6_reliability.py; results/g4_detection_vision_t03.json; results/g5_recovery_vision.json; results/g6_reliability.json

## Slide 9
HONEST LIMITATIONS
Scope of validity
09
SIMULATION FIDELITY
Kinematic carry model;
no physics-based grasping.
DETERMINISTIC EVIDENCE
Fixed seeds, noise = 0;
no confidence interval.
TEST COVERAGE
One disturbance type,
one target position.
DEPLOYMENT BOUNDARY
MuJoCo + CPU only;
no real hardware or certification.
CONTROLLED SIMULATION EVIDENCE ≠ FORMAL PROOF
Notes: We use honest scope accounting. This is controlled simulation evidence, not a formal proof. Grasping uses a kinematic carry model, trials use fixed seeds with noise equal to zero, and only one disturbance type and one target position have been validated. There is no real-hardware deployment or safety certification yet.
Evidence: results/FINAL_REPORT.md, Scope of Validity

## Slide 10
CONCLUSION
RESILIENCE
> SPEED
Under the tested scenario, governed execution recovered
10 / 10 while open-loop execution recovered 0 / 10.
01
OBSERVE CHANGE
02
REPLACE STALE PLAN
03
PRESERVE EVIDENCE
CLONE • RUN • INSPECT
github.com/rootz-synapsa/roboguardian
SCAN TO CLONE
OPEN SOURCE
Notes: RoboGuardian demonstrates that, under this tested scenario, governed execution is more resilient than open-loop execution when the world changes. The result is not a speed claim: it is a recovery and evidence claim. The code is open source—scan the QR code to clone, run, and inspect it. Thank you.